## Slide 1
Introduction to Computer Networks 22CS008
Data Link Layer
Lecture10-11 (Theory)
Dr. Htet Ne Oo
Department of Computer Science and Engineering,
Chitkara University, Punjab

## Slide 2
Index
,
Redundancy
Error Detection
Error Correction

## Slide 3: Redundancy
Instead of repeating the entire data stream, a shorter group of bits may be appended to the end of each unit.
This technique is called Redundancy because the extra bit are redundant to the information. They are discarded as soon as the accuracy of the transmission has been determined.

## Slide 4: Types of Redundancy Checks
There are basically four types of redundancy checks.
  1. VRC (Vertical Redundancy Check).
  2. LRC (Longitudinal Redundancy Check).
  3. CRC (Cyclical Redundancy Check).
  4. Checksum

## Slide 5
Four types of redundancy checks are used in data communications

## Slide 6
Cyclic Redundancy Check
CRC Generation at sender side
Find the length of divisor ‘L’
(divisor is already agreed between sender and receiver)
Append ‘L-1’ bits to the original message
Perform binary division operation
Remainder of the division = CRC
Note: CRC must be of ‘L-1’ bits.
For binary division, XOR is used.

## Slide 7
Cyclic Redundancy Check
CRC Verification at receiver side
Received original message appended with CRC
Perform binary division operation as in sender side
If the remainder is all ‘0’s, then the message is not corrupted during transmission

## Slide 8
Binary Division

## Slide 9
Polynomial
Sometimes, the divisor can be in the form of polynomial also.

## Slide 10
Polynomial and Divisor

## Slide 11
Hamming Code

## Slide 12
Hamming Code Algorithm
General Algorithm of Hamming code: Hamming Code is simply the use of extra parity bits to allow the identification of an error.
Write the bit positions starting from 1 in binary form (1, 10, 11, 100, etc).
All the bit positions that are a power of 2 are marked as parity bits (1, 2, 4, 8, etc).
All the other bit positions are marked as data bits.

## Slide 13
Hamming Code Algorithm
4. Each data bit is included in a unique set of parity bits, as determined its bit position in binary form.
a. Parity bit 1 covers all the bits positions whose binary representation includes a 1 in the least significant position (1, 3, 5, 7, 9, 11, etc).
b. Parity bit 2 covers all the bits positions whose binary representation includes a 1 in the second position from the least significant bit (2, 3, 6, 7, 10, 11, etc).
c. Parity bit 4 covers all the bits positions whose binary representation includes a 1 in the third position from the least significant bit (4–7, 12–15, 20–23, etc).

## Slide 14
Hamming Code Algorithm
d. Parity bit 8 covers all the bits positions whose binary representation includes a 1 in the fourth position from the least significant bit bits (8–15, 24–31, 40–47, etc).
e. In general, each parity bit covers all bits where the bitwise AND of the parity position and the bit position is non-zero.

## Slide 15
Hamming Code Algorithm
5. Since we check for even parity set a parity bit to 1 if the total number of ones in the positions it checks is odd.
6. Set a parity bit to 0 if the total number of ones in the positions it checks is even.

## Slide 16
Hamming Code Algorithm

## Slide 17
Hamming Code

## Slide 18
Hamming Code

## Slide 19
Example of Hamming Code

## Slide 20
Single-bit error

## Slide 21
Error Detection

## Slide 22
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2
2. The Hamming distance d(10101, 11110) is 3 because

## Slide 23
Find the minimum Hamming distance of the coding scheme in Table
Solution
We first find all Hamming distances.
Example
The dmin in this case is 2.

## Slide 24: Thank You

## Slide 25: Break Time

## Slide 26: Checksum
Checking the sum of data words
1. Divide the data streams into equal size blocks
2. Do binary addition of those blocks
3. If there is carry bit, add that carry bits also.
4. Do 1’s complement (Changing 1 to 0, or 0 to 1)
Bit stream
10110011 10101011 01011010 11010101
10110011
10101011
01011010
11010101
Receiver side, do the addition process including check sum result.
If all ‘1s’ the data error free and accepted. Else it will be discarded.